## Slide 1: Virtual Machines
What is a virtual machine?
  A computer with the operating system and added software that does not on dedicated hardware
  Multiple VMs can run on the same physical hardware server and share its resources
  To the network each PC seems just like a stand-alone one

## Slide 2: Virtual Machines
Where does this meet our business?
  IT users purchase very powerful hardware server and attempt to run as many virtual PCs on those
  The requirement to run NVRs on such machines is growing
  This is less relevant for display stations (workstations and VMDC) as these are considered users PC and not servers

## Slide 3: Virtual Machines
Advantages:
  Hardware cost is shared by multiple servers
  Redundancy solutions can be offered
  Saves space, power and HVAC resources

## Slide 4: Virtual Machines
Disadvantages
  Physical server prices are very high
  VMs tend to be under powered if too many share the physical server
  Setup and resource allocation need to be done with attention to system needs

## Slide 5: Virtual Machines
Where do we stand?
  Vicon does not test nor approve specific VMs (there is an unlimited number of combinations)
  Our recommendation is as follows:
    Ensure the VM meets the minimum requirements for NVR
    Verify you have a network card dedicated to the NVR and not shared by others
    Verify the hard drives for recording are dedicated and not shared
    Verify that the overall load on the physical server is balanced as NVRs take much more resources to run than typical IT servers
    Currently VM redundancy has not been tested but should be supported